## Slide 1
TOPIC : “TriSense: A Gesture, Voice and Face-Based Contactless PC Control System with Arduino Feedback”
Bharati Vidyapeeth
(Deemed to be University)
College of Engineering, Pune
ROLL NO. | NAME | PRN
21 | Amit Gadade | 2514110443
22 | Piyush Kapile | 2514110444
28 | Kumar Pratyush | 2514110450
31 | Basavaraj Kammar | 2514110453
33 | Shravan Chandore | 2514110455
DEPARTMENT OF INFORMATION TECHNOLOGY
Under the guidance of
Prof. Prakash Devale

## Slide 2
Project Overview
TriSense lets you control a Windows PC without touching it: hand gestures, voice commands and face/head movement become actions like volume, scroll, screenshot and lock.
The laptop does the heavy processing. An Arduino Uno acts as a physical control panel that switches modes and shows live feedback.
Gesture
Voice
Face

## Slide 3
How It Works
LAPTOP (Python)
OpenCV + MediaPipe: hand gestures, face/head tracking, blink click
Vosk: offline voice recognition
pyautogui: volume, scroll, screenshot, lock
Flask dashboard: live command log, mode toggles
ARDUINO UNO (control panel)
Push button cycles the modes (Gesture / Voice / Face)
4 LEDs show the mode and errors
16x2 I2C LCD shows the mode and last command
Clone board with CH340 USB chip
MODE · CMD · ERR
READY
BTN:PRESSED
USB serial · 9600 baud · text messages TYPE:VALUE

## Slide 4
Key Components
1
Laptop (Python)
Runs OpenCV, MediaPipe, Vosk, pyautogui and Flask
2
Arduino Uno
Physical control panel over USB serial (9600 baud)
3
16x2 I2C LCD
Shows the current mode and the last command
4
4 LEDs + 220 ohm resistors
Blue, green, yellow = mode; red = error
5
Push Button + Breadboard
Cycles modes; solder-free wiring with jumper wires
Arduino Uno (CH340 clone)

## Slide 5
Arduino Wiring (Breadboard, No Soldering)
LCD (I2C)
GND
→
GND
VCC
→
5V
SDA
→
A4
SCL
→
A5
Address 0x27 (try 0x3F if blank)
Library: LiquidCrystal_I2C
LEDs (220 ohm to GND)
D8
Gesture
D9
Voice
D10
Face
D11
Error
Push Button
D2 → GND
Use INPUT_PULLUP: LOW = pressed
Debounce the button in code
Each press switches to the next mode

## Slide 6
Software Modules
Gesture Engine
Person A
MediaPipe hand tracking: volume, mute, play/pause, next/prev, scroll, zoom
Voice Engine
Person B
Vosk offline speech recognition: open apps, screenshot, lock, media
Face / Head Tracking
Person C
Head moves the cursor, blink = click, face command for lock
Arduino + Dashboard
Person D
Firmware, serial bridge and Flask dashboard (command log, mode toggles)
Only D needs the Arduino. A, B and C develop on the laptop and print their detections.

## Slide 7
Serial Message Contract
9600 baud
TYPE:VALUE
ALL CAPS, no spaces
Value max 12 chars
Ends with newline
Python → Arduino
Arduino → Python
MODE:GESTURE | VOICE | FACE
Sets the active mode
CMD:<name>
Shows last command on LCD line 2
ERR:<reason>
Red LED + LCD, e.g. ERR:NO_MIC
READY
Arduino booted; Python replies MODE:GESTURE
BTN:PRESSED
Button pressed; switch to the next mode
Rules: send events only (no streams) · 0.5 s cooldown per command · max about 10 messages/s
Only one program can use the COM port, so close the Arduino Serial Monitor before running Python

## Slide 8
Official Command Names
Shared
VOLUP
VOLDOWN
MUTE
PLAYPAUSE
NEXT
PREV
Gesture
SCROLLUP
SCROLLDOWN
ZOOMIN
ZOOMOUT
Voice
OPEN_CHROME
OPEN_NOTEPAD
SCREENSHOT
LOCK
Face
CLICK
LOCK
Test output while building alone: [GESTURE] VOLUP [VOICE] OPEN_CHROME [FACE] CLICK
Cursor movement is not sent to the Arduino (too many messages)

## Slide 9
Arduino Feedback Panel
MODE: VOICE
Last: VOLUP
16x2 I2C LCD: line 1 = mode, line 2 = last command
Button press cycles the mode
GESTURE
→
VOICE
→
FACE
LED indicators
Blue · D8
Gesture mode
Green · D9
Voice mode
Yellow · D10
Face mode
Red · D11
Error
Data flows both ways: Python → Arduino (status) and Arduino → Python (button press)

## Slide 10
Development Roadmap
0
Setup
GitHub/shared folder, install libraries, agree on the contract
1
Modules alone
Each prints [SOURCE] COMMAND; Arduino hello, LEDs, button, LCD
2
Main controller
Combines modules, performs PC actions, switches modes
3
Connect Arduino
Button → mode change → LCD and LED update
4
Flask dashboard
Command log and mode toggles
5
Test and tune
Lighting, noise and false triggers
6
Final prep
Freeze features, report, backup demo video, viva practice
Final outcome
Working model, demo and viva

## Slide 11
Hardware Status and Budget
Done
Arduino IDE 2.3.10 installed
Board tested with the Blink example on a Windows laptop
Lesson learned
COM3 was the laptop's internal Intel port; the Arduino was COM6. Check Device Manager before selecting a port.
Still to buy
about Rs 330–555
16x2 I2C LCD
4 LEDs
220 ohm resistors
Push buttons
830-point breadboard
Male-male and male-female jumper wires

## Slide 12: Future Possible Upgradation
This PBL which is having a small scope now, can be extended/upgraded with following features (possible PBL for Sem-VI/VII) :
Add more gestures and user-defined custom commands
Replace the USB cable with Bluetooth/Wi-Fi (HC-05 or ESP32)
Multi-language and noise-robust voice commands
Eye-gaze cursor control and smoother head tracking
Mobile app dashboard and multi-device control

## Slide 13
Thank You
TriSense: Gesture · Voice · Face
Questions?